Setting up a client to a remote loop-back server

This workbook will describe the steps to setup a client on the Arduino with a SparkFun ESP8266 AT WIFI Shield and connect to a remote server application loop.c . It will describe the setup, but also the issues and learning that was obtained during the project.

Paul van Haastrecht
January 2018

# 1. Software
The test has been performed with the Arduino IDE 1.8.6.

It requires the enhanced version of the Sparkfun ESP8266 AT WIFI shield library from github
https://github.com/paulvha/PVH_ESP8266_AT_Arduino_Library

This needs to be installed as any other IDE library. (there is enough documentation around that) Install the library, restart the IDE.

For the remote server and separate test program is developed in C-language: loop.c. This program has successfully been used on the Raspberry PI and Ubuntu. It is placed in the “extra” folder of the library.

# 2. Hardware

I have used an Arduino Uno and a Sparkfun ESP8266 WIFI Shield. ( https://www.sparkfun.com/products/13287) .

An extra power-supply. It turned out that my USB was not providing enough power for a stable configuration. So I added a 6V/2A external power supply to the Arduino input.

# 3. Software setup

## 3.1 Setup client sketch
Obtain the example :
File, Examples, (scroll down) PVH_ESP8266_AT , pvh_ESP8266_Shield_client

Save this for your self : File, save-as (give it a name)

Look for :
////////////////////////////////////////////
// WiFi Network Definitions //
///////////////////////////////////////////
// Replace these two character strings with the name and
// password of your WiFi network.
const char mySSID[] = "yourSSIDhere";
const char myPSK[] = "yourPWDhere";

You MUST change to set mySSID to your SSID network name and myPSK to the password in order to connect.

Look for :

//////////////////////////////////////////////////////////////////////
// set new static IP if wanted //
// Default : no change wanted //
// Change #define ipaddress "" //
// to something like #define "192.168.1.161"; //
//////////////////////////////////////////////////////////////////////
#define ipaddress ""

char CLIENTIP[]= ipaddress;
char gateway[]="192.168.1.1";
char mask[]="255.255.255.0";

You can change the client IP address that was provide by the access point to a static address, set the ipaddress definition different than empty, as indicated.

WARNING: The first 3 octets of the IP and the gateway ( by default: “192.168.1”) must be equal and the same as your local wireless has. This can be found after starting the sketch as it will display the IP address it got once connected OR by starting the ‘loop’ server program that will display the IP and port to connect to.

Look for :
///////////////////////////////////////////////////////////////////////////
// Remote server IP address and port to connect to //
///////////////////////////////////////////////////////////////////////////
char SERVERIP[]= "192.168.1.137";
#define _port 333

This is the IP address of the server you want to connect to. If you change the server_port number, you will also have to change this in loop.c (PORT).

Look for :

////////////////////////////////////////////
// Welcome Message to sent //
////////////////////////////////////////////
const char message[] = "Hallo there\n";

This is the welcome message that will be sent to the server once connected. Loop.c will sent received messages back to the Arduino/serial monitor.
## 3.2 Setup Debug
A new feature with this driver is to see what information is exchanged between the Arduino and ESP8266. In the setup(),

  // enable debug data from driver
  // (0 = disable (default), 1 = show commands, 2 = detailed)
 esp8266.debug(0);

0 is default (actually you do not need to call it),
1 will show which commands are sent to the ESP8266. This will align with the ESP8266 AT
    documentation (which is also stored in the “extra” directory of the library)
2 will show next to the commands, the feedback from the ESP8266. The format for each line:
btb C H B \n
btb: byte to buffer routine
C : character as received
H : hex value of the character
B : buffer index

With option 2 it might be hard to see at the serial output as a lot of information is flowing over the screen, but you can pause that and scroll back by disabling auto scroll bottom left in the IDE serial monitor.
## 3.3 Setup server software
The loop.c has been tested under Linux on the Raspberry Pi-3 and Ubuntu. To compile on the Raspberry Pi: cc -o loop loop.c With little changes (e.g. getopt) it could be made to work
also under windows.
# 4. Hardware setup
## 4.1 Setup ESP8266

Set the switch for the serial connection on the ESP8266 to SW (softserial), otherwise it will not work. I have connected the Arduino Stackable Header Kit, so it connects directly to the board.

In my situation the configuration was unstable as the USB was not able to provide enough power from my Ubuntu PC. Hence I connected an external power supply ( 6V / 2A). It became much better, but still my ESP8266 was not always reacting as I hoped.

# 5. Starting Software
## 5.1 Starting the server application : loop

After compiling start the application with : ./loop
An optional argument ‘-v’ can be provided to show the received bytes in Hex.

After starting it will display information like:
connect to etho:	192.168.1.142, port 333
connect to Wlan0:	192.168.1.137, port 333

waiting for client’s request ……..

The number of IP options to connect to is depending on the number of network controllers. In my case (raspberry Pi-3) I have the network cable (eth0) and wireless(Wlan0) connection active. It also shows the port to connect to, that must match what is in the sketch. Now it just waits for a client to connect…

## 5.2 Starting the Arduino

After compiling and loading the sketch, open the serial monitor. It will show :

Press any key to begin.

This is to make sure you are present. After pressing < enter> you should see the following sequence

starting initializing
ESP8266 Shield Present
ESP8266 speed set to 19200
ATversion : 0.30.0.0(Jul 3 2015 19:35:49)
SDKversion : 1.2.0
CompileTime : Jul 7 2015 18:34:26
starting connect to WiFi
Mode set to station
Try to detect <SSID>
(4,"<SSID>",-53,"c0:c1:c0:58:ca:e3",1,0)
Connecting to <SSID>
My IP : 192.168.1.107
My MAC: 5c:cf:7f:e3:5d:11
Connected to: <SSID>
My new static IP: 192.168.1.161

Press any key to connect as client.

The <SSID> will show the ssid for the network that you have set in the sketch. The line “My new static IP: 192.168.1.161” will only show up if you requested a static IP in the sketch setup, as I did.

NOTE
Sometimes however, much more than I wanted, my board was not reacting (this can be seen with setting debug to 2). This was mostly caused in what operating state the board left behind before starting this sketch. If it ends with something like:
Error during stopping server.
Error: 0
Looping forever.
The best way is to close the serial monitor, and re-open the serial monitor and try again. Sometimes I had to do so 3 times, sometimes I had to re-compile and reload, sometimes I had to remove the USB (and power connection) wait 10 seconds for a hard reset. Using the reset switch does not do ANYTHING, other than reboot the Arduino.

WARNING: IF YOU REMOVE AND REAPPLY POWER, MAKE SURE THAT THE SERIAL MONITOR IS CLOSED. OTHERWISE IT WILL NOT RE-CONNECT ON THE SAME USB PORT

If you now press <enter> in the serial monitor the following should show:

connected to server: 192.168.1.137
Hallo there

The last line is the echo back from the server application ‘loop’.

# 6. Working together

After starting the Arduino client you should see the following on the server application :
TCP client connected
client from 192.168.1.161
ready to communicate
Received : Hallo there
now sending back : Hallo there

Now in the serial monitor type : hallo < enter>
it will show
Sending: hallo

receiving: hallo

On the server screen you’ll see
Received : hallo
now sending back : hello

This can continue as long as you like, but there are 2 special commands

CLOSE <enter> (in capitals). This will send CLOSE to the server which will display a message:
Client decided to close connection for now

The Arduino will display the following:

Closing connection
Connection closed

Press any key to connect as client.

STOP <enter> (in capitals). This will send STOP to the server which will display a message:
Client stopped the application

The Arduino will display the following:

Stopping connection
Error: 0
Looping forever.
Stop will close the wireless connection and reset the board, so that at a next start it should be available again.