Setting up a server for loopback or talkback

This workbook will describe the steps to take setup a server can loopback (echo) the received information or the basics of a chat (talkback). It will describe the setup, but also the issues and learning that was obtained during the project.

Paul van Haastrecht
January 2018

# 1. Software
The test has been performed with the Arduino IDE 1.8.6.

It requires the enhanced version of the Sparkfun ESP8266 AT WIFI shield library from github
https://github.com/paulvha/PVH_ESP8266_AT_Arduino_Library

This needs to be installed as any other IDE library (there is enough documentation around that.). Install the library, restart the IDE.

For the remote client and separate test program is developed in C-language.: tclient.c. It is available in the “extra” folder of the library. This program has successfully been used on the Raspberry PI and Ubuntu.
# 2. Hardware

I have used an Arduino Uno and a Sparkfun ESP8266 WIFI Shield.
 ( https://www.sparkfun.com/products/13287) .

# 3. Software setup
## 3.1 Setup as a server on your network

Obtain the example :
File, Examples, (scroll down) PVH_ESP8266_AT , pvh_ESP8266_Shield_loopback_gpio
or pvh_ESP8266_Shield_talkback_gpio.

Save this for your self : File, save-as (give it a name)

Look for :
////////////////////////////////////////////
// WiFi Network Definitions //
///////////////////////////////////////////
// Replace these two character strings with the name and
// password of your WiFi network.
const char mySSID[] = "yourSSIDhere";
const char myPSK[] = "yourPWDhere";

You MUST change to set it to your SSID name and password in order to connect.
### 3.1.1 In pvh_ESP8266_Shield_loopback_gpio
uint16_t server_port = 333;

If you change the server_port number, you will also have to change this in tclient.c (PORT_LOOP).

### 3.1.2 In pvh_ESP8266_Shield_talkback_gpio
uint16_t server_port = 334;

If you change the server_port number, you will also have to change this in tclient.c (PORT_TALK).

### 3.1.3. Difference between loopback and talkback
The difference between loopback and talkback, is that in loopback the received information is returned to the client, in talkback the information typed in the serial monitor is sent (like a chat).
## 3.2 Setup Debug
A new feature with this driver is to see what information is exchanged between the Arduino and ESP8266. In the setup(),

  // enable debug data from driver
  // (0 = disable (default), 1 = show commands, 2 = detailed)
 esp8266.debug(0);

0 is default (actually you do not need to call it),
1 will show which commands are sent to the ESP8266. This will align with the ESP8266 AT
    documentation (which is also stored in the extra directory of the driver)
2 will show next to the commands, the feedback from the ESP8266. The format for each line:
btb C H B \n
btb: byte to buffer routine
C : character as received
H : hex value of the character
B : buffer index

With option 2 it might be hard to see at the serial output as a lot of information is flowing over the screen, but you can pause that and scroll back by disabling auto scroll bottom left in the IDE serial monitor.

## 3.3 Setup Client software
The tclient.c has been tested under Linux on the Raspberry Pi-3 and Ubuntu. To compile on the Raspberry Pi: cc -o tclient tclient.c. With little changes (e.g. getopt) it could be made to work
also under windows.

# 4 Hardware setup
## 4.1 Setup ESP8266

Set the switch for the serial connection on the ESP8266 to SW (softserial), otherwise it will not work. I have connected the Arduino Stackable Header Kit, so it connects directly to the board. I had issues with that it would not connect. For that I have include txpower() in the sketch (see later “software insights in sketch”)

# 5. Software usage
## 5.1 Starting server
After setting the parameters, compile and loading to the Arduino. Then open the serial monitor for 9600 baud connection (default)

The first message is : Press any key to begin.

This is waiting on your presence . After pressing <enter> the following sequence will appear

initializing ESP8266
ESP8266 Shield Present
Stop any server running + board reset ( 2 - 3 seconds)
ATversion : 0.30.0.0(Jul 3 2015 19:35:49)
SDKversion : 1.2.0
CompileTime : Jul 7 2015 18:34:26
start connecting
Mode set to station
Try to detect <SSID>
(4,"<SSID> ",-52,"c0:c1:c0:58:ca:e3",1,0)
Connecting to <SSID>
My IP : 192.168.1.107
My MAC: 5c:cf:7f:e3:5d:11
Connected to: <SSID>

Press any key to start server.

<SSID> is your SSID, it will show the SSID you have set for your network. If that connection fails all the time, check your network SSID and Password. If that keeps failing, maybe you have a weak signal. The sketch will try to detect your SSID and show information (documented in the sketch and below in “Software insights in Sketch”)

After pressing <enter> you will something like:
loopback :	Server started! Go to 192.168.1.107 port : 333
talkback :	Server started! Go to 192.168.1.107 port : 334 (Different port!!)

Watch the IP address , as you need that later on for the command line on your client application

NOTE
Sometimes however, much more than I wanted, my board was not reacting (this can be seen with setting debug to 2). If it ends with something like:
Error during stopping server.
Error: 0
Looping forever.
The best way is to close the serial monitor and re-open the serial monitor and try again. Sometimes I had to do so 3 times, sometimes I had to re-compile and reload, sometimes I had to remove the USB for a hard reset. Using the reset switch does not do ANYTHING, other than reboot the Arduino.

WARNING: IF YOU REMOVE AND REAPPLY POWER, MAKE SURE THAT THE SERIAL MONITOR IS CLOSED. OTHERWISE IT WILL NOT RE-CONNECT ON THE SAME USB PORT

## 5.3 Client setup
### 5.3.1 loopback
To start the client connection, type ./tclient -l <IP-address> (lowercase ‘L’)
Taken the examples above running as Server : ./tclient -l 192.168.1.107

The port (333) is hard coded in the program and chosen as you select -l option.

### 5.3.2 talkback
To start the client connection, type ./tclient -t <IP-address>
Taken the examples above running as Server : ./tclient -t 192.168.1.107

The port (334) is hard coded in the program and chosen as you select -t option.
# 6. Using software
Once you started the client on the serial monitor from the Arduino you should see
Client detected
Loop back client connected!

If NOT, press CONTROL-C on the client to exit the tclient and try to connect the tclient again.

NOTE:
If the client show “connect error”, most of the time the ESP8266 server has not been started and waiting on you to press enter. (happened to me more than once).

WARNING: IT WILL TAKE SOMETIME BEFORE THE SERVER STARTS, BUT ALSO SOMETIME AFTER THE CLIENT DISCONNECT AND CAN CONNECT AGAIN.
WAIT 10 SECONDS AFTER SERVER START OR DISCONNECT TO (RE) CONNECT.

## 6.1.1 loopback
On the client you should see :
Loop back demo
to remote :

As example you type : hallo <enter>

sending
waiting for echo

received: hallo

to remote:

On the serial monitor you’ll see:

Client detected
Loop back client connected!
Received : hallo

## 6.1.2 talkback

On the client you should see:
Talking back demo
to remote:

As example you type :
to remote : hallo <enter>
to remote: all OK? <enter>
to remote:

On the serial monitor you’ll see:

Client detected
Talk back client connected!
FROM: hallo
FROM: all OK ?

As example in the serial monitor you type : yes < enter>
On the serial monitor now :

Client detected
Talk back client connected!
FROM: hallo
FROM: all OK ?
TO : yes

On the client screen now:
to remote : hallo <enter>
to remote: all OK?
received : yes
to remote:

P.s. Loopback & Talkback sketch have a time out after 1 minute of no activity.
# 7. Software insights in the Sketch
Sharing some aspects of the software to share.

Setup()
The esp8266.debug() See the debug information in the chapter setting up software

initializeESP8266()
The esp8266.tcpStopServer() is a new feature. When setting up as a server we want to be able to potentially switch to different port than the current. This can only be done if we first STOP a potential current server. Stopping means also a reset, which takes time and it is important to wait for proper reset.

The esp8266.txpower(ESP8266_POWER_SET, 40) is a new feature. It allows to set the transmitter power in steps of 0.25db. The value can be between 0 and 82. Setting it to the highest power however, while using the on-board antenna, caused communication issues. However it solved the issue that I was hardly able with the shield directly connected on the Arduino to connect to my network. More experimenting should be done to find the right signal strength.

With the setSpeed(19200) subroutine you can change the softSerial() speed of communication between the ESP8266 and Arduino. Most of the time the 9600 default is good enough, but you can change it with this example.

With setDHCP() the ESP8266 is instructed to obtain an IP address from the access point.

With setstatic() one get set a static address on the server. You must call setDHCP() in a later sketch if you want the IP address from the access point.

The checkssid(int disp) will check whether the requested SSID is available and display information about the network : The output is raw format : (4,"homelan",-45,"c0:c1:c0:58:ca:e3",1,0)
 4 : WPA_WPA2_PSK
        0 OPEN
        1 WEP
        2 WPA_PSK
        3 WPA2_PSK
        4 WPA_WPA2_PSK

 homelan : SSID of AP
 -45 : signal strength
 “c0:c1:c0:58:ca:e3" : MAC address
 1 : channel
 0 : <freq offset> frequency offset of AP,unit:KHz.
        <freq offset> / 2.4 to get unit ppm”

The firmware_info() subroutine will obtain the firmware information from the ESP8266.

DisplayConnectInfo() will display the MAC, IP and access point

# 8. Software insights in the driver
A large number of changes have applied for the driver and are documented in a separately.

## 8.1 RAM space
Important for this project was the on-going challenge with RAM space. The final version had a constant warning on low memory available, but all worked well:

Build options changed, rebuilding all
Sketch uses 15350 bytes (47%) of program storage space. Maximum is 32256 bytes.
Global variables use 1360 bytes (66%) of dynamic memory, leaving 688 bytes for local	variables. Maximum is 2048 bytes.

Part of this is because of the extended features and improvements in the driver. There is a way however to reduce that impact in the file PVH_ESP8266WiFi.h, near the top around line 70, you can remove the comments slashes before : //#define ESP_LIGHT 1 to : #define ESP_LIGHT 1.
Save that, recompile the sketch.

This will create a lighter version of the driver by removing features and reduce the buffer (now that these features are removed). Those features are NOT used in this sketch, but might be in other sketches who than fail if you try them later on. It will help for about 120 bytes of RAM.

## 8.2 SoftSerial
A word about SoftSerial as it has caused me a bit of headache when working on firmware_info()

Although with the command AT_GMR you obtain the build information, the Softserial standard receivebuffer is 64.

Defined in …./arduino-nightly/hardware/arduino/avr/libraries/SoftSerial/src/SoftwareSerial.h
  #define _SS_MAX_RX_BUFF 64

That is on the boundary. WHY ? well SoftwareSerial is interrupt driven, as soon as the input level changes, disables that interrupt, trigger a careful time-based checking on the input level to capture the 8 bits, store the byte in it’s buffer and enable interrupt.

This is handled by the SAME processor as the code below, which will get hardly time to read from that softSerial buffer. As such with the call to get firmware the buffer could fill up easily to more than 64 bytes the receivebuffer causing the program to get lost. Extending the buffer to 256 will enable to capture more input, but whether it will overrun is depending on the amount of detected SSID. The buffer could be extended more, but it will take more RAM space.

Note : IN MANY OF MY TEST I HAVE SET THE SOFTSERIAL TO 128 BYTES TO IMPROVE STABILITY.