Setting up a SoftAP server for loopback

This workbook will describe the steps to setup a softAP server that can loopback (echo) the received information. It will describe the setup, but also the issues and learning that was obtained during the project.

Paul van Haastrecht
January 2018

# 1. Software
The test has been performed with the Arduino IDE 1.8.6.

It requires the enhanced version of the Sparkfun ESP8266 AT WIFI shield library from github
https://github.com/paulvha/PVH_ESP8266_AT_Arduino_Library

This needs to be installed as any other IDE library. (there is enough documentation around that) Install the library, restart the IDE.

For the remote client and separate test program is developed in C-language.: tclient.c. It is available in the “extra” folder of the library. This program has successfully been used on the Raspberry PI and Ubuntu.

# 2. Hardware
I have used an Arduino Uno and a Sparkfun ESP8266 WIFI Shield.
 ( https://www.sparkfun.com/products/13287) .

# 3. Software setup
## 3.1 Setup server as SoftAP
Obtain the example :
File, Examples, (scroll down) PVH_ESP8266_AT , pvh_ESP8266_SoftAP_loopback

Save this for your self : File, save-as (give it a name)

Look for :
///////////////////////////////////////////
// ESP8266Server definition //
///////////////////////////////////////////
// (This is only global because it's called in both setup() and loop()).
// CHANGE BELOW TO SET YOUR OWN SSID AND PASSWORD
char serverSSID[]="testserver"; // name
char serverPSK[]="sparkfun"; // password
uint16_t server_port = 333;

You do NOT have to change it, but you can change the SSID network name and/or password. If you change the server_port number, you will also have to change this in tclient.c (PORT_LOOP).
## 3.2 setup for different IP
Look for :
////////////////////////////////////////////////////////////////////////////
// set new newSoftIP[]= "" if no change wanted //
///////////////////////////////////////////////////////////////////////////
char newSoftIP[] = "";
//char newSoftIP[]="192.168.2.100"; // new IP address.
char newSoftGateway[] ="192.168.2.1"; // new Gateway
char newSoftMask[]="255.255.255.0"; // new Mask

If you want to change the default SoftAP IP address you can do so.
Comment : //newSoftIP[] =””
Uncomment the example: char newSoftIP[] = “192.168.2.100” and adjust your IP.
## 3.3 Setup for different MAC
Look for:
//////////////////////////////////////////////////////////////////////////////////////////////////////////////
// //
// SOFT MAC SHOULD BE UNIQUE AND NOT EQUAL TO ANY //
// OTHER MAC ON THE NETWORK, INCLUDING THE HARDWARE //
// MAC OF THE ESP8266 //
// //
        // set new newSoftMAC[]= "" if no change wanted //
        ///////////////////////////////////////////////////////////////////////////////////////////////////////////////
char newSoftMAC[] = "";
//char newSoftMAC[]="5e:cf:7f:e3:7F:11"; // new MAC address.

If you want to change the default SoftAP MAC you can do so.
Comment : //char newSoftMAC[]=””
Uncomment the example: char newSoftMAC[]="5e:cf:7f:e3:7F:11" and adjust your MAC.
## 3.4 Setup Debug
A new feature with this driver is to see what information is exchanged between the Arduino and ESP8266. In the setup(),

  // enable debug data from driver
  // (0 = disable (default), 1 = show commands, 2 = detailed)
 esp8266.debug(0);

0 is default (actually you do not need to call it),
1 will show which commands are sent to the ESP8266. This will align with the ESP8266 AT
    documentation (which is also stored in the extra directory of the driver)
2 will show next to the commands, the feedback from the ESP8266. The format for each line:
btb C H B \n
btb: byte to buffer routine
C : character as received
H : hex value of the character
B : buffer index

With option 2 it might be hard to see at the serial output as a lot of information is flowing over the screen, but you can pause that and scroll back by disabling auto scroll bottom left in the IDE serial monitor.

## 3.5 Setup Client software
The tclient.c has been tested under Linux on the Raspberry Pi-3 and Ubuntu. To compile on the Raspberry Pi: cc -o tclient tclient.c. With little changes (e.g. getopt) it could be made to work
also under windows.

# 4 Hardware setup
## 4.1 Setup ESP8266
Set the switch for the serial connection on the ESP8266 to SW (softserial), otherwise it will not work. I have connected the Arduino Stackable Header Kit, so it connects directly to the board. I had issues with that it would not connect. For that I have include txpower() in the sketch (see later “software insights in sketch”)
# 5. Software usage
## 5.1 Starting as SoftAP
After setting the parameters, compile and loading to the Arduino. Then open the serial monitor for 9600 baud connection (default)

The first message is : Press any key to begin.

This is waiting on your presence . After pressing <enter> the following sequence will appear

initializing ESP8266
ESP8266 Shield Present
Stop any server running + board reset ( 2 - 3 seconds)
initializing Access Point
Mode set to SoftAP and station

Press any key to start server.

After pressing <enter> you will see something like:

Server timeout 60
Connect to address : 192.168.4.1 port for GPIO test : 333

Watch the IP address , as you need that later on for the command line on your client application

NOTE
Sometimes however, much more than I wanted, my board was not reacting (this can be seen with setting debug to 2). This was mostly caused in what operating state the board left behind before starting this sketch. If it ends with something like:
Error during stopping server.
Error: 0
Looping forever.
The best way is to close the serial monitor and re-open the serial monitor and try again. Sometimes I had to do so 3 times, sometimes I had to re-compile and reload, sometimes I had to remove the USB for a hard reset. Using the reset switch does not do ANYTHING, other than reboot the Arduino.

WARNING: IF YOU REMOVE AND RE-APPLY POWER, MAKE SURE THAT THE SERIAL MONITOR IS CLOSED. OTHERWISE IT WILL NOT RE-CONNECT ON THE SAME USB PORT

## 5.2 Client connection setup
You must login to this access point from your the remote PC/Raspberry Pi .
WARNING : You will have to check this every time you restart the program !!
Your remote PC/Raspberry Pi must be connected wireless (as this is a wireless access point) and look for the SSID with the name you selected (default: testserver). Select that and enter the password that you have set (default: sparkfun). If will take sometime to connect.

If it can not find the SSID, try refresh the list, try to get closer to the Arduino and shield, change the angle a bit. If that does not work, look whether you see the SSID on your smart-phone. There are also special programs that show available SSID’s. If NOT found, restart the server, close the serial monitor and start again. If you see it, but can not login, check your password, check the signal strength etc.

To start the client connection, type ./tclient -l <IP-address> (lowercase ‘L’)
Taken the examples above running as Server : ./tclient -l 192.168.4.1

The port (333) is hard coded in the program and chosen as you select -l option.

# 6. Using software
About every 10 seconds the server will display who is connected to the server, NOT who has a socket opened. So once you logged on to the Access Point, every 10 seconds you should see in the serial monitor something like

Connected to Access Point:
   IP , MAC
192.168.4.2,b8:27:eb:1a:7e:34
This has been done to show it can be done :-)

As soon as the tclient has started you should see :

Client detected
Loop back client connected!
If NOT, press CONTROL-C on the client to exit the tclient and try to connect the tclient again.

NOTE:
If the client show “connect error”, most of the time the ESP8266 server has not been started and waiting on you to press enter. (happened to me more than once).

WARNING: IT WILL TAKE SOMETIME BEFORE THE SERVER STARTS, BUT ALSO SOMETIME AFTER THE CLIENT DISCONNECT AND CAN CONNECT AGAIN.
WAIT 10 SECONDS AFTER SERVER START OR DISCONNECT TO (RE) CONNECT.

## 6.1 loopback
On the client you should see :
Loop back demo
to remote :

As example you type : hallo <enter>

sending
waiting for echo

received: hallo

to remote:

On the serial monitor you’ll see:

Client detected
Loop back client connected!
Received : hallo

P.s. Loopback & Talkback sketch have a time out after 1 minute of no activity.
# 7. Software insights in the Sketch

Sharing some aspects of the software to share.

Setup()
The esp8266.debug() See the debug information in the chapter setting up software

initializeESP8266()
The esp8266.tcpStopServer() is a new feature. When setting up as a server we want to be able to potentially switch to different port then the current. This can only be done if we first STOP a potential current server. Stopping means also a reset, which takes time and it is important to wait for proper reset.

The esp8266.txpower(ESP8266_POWER_SET, 40) is a new feature. It allows to set the transmitter power in steps of 0.25db. The value can be between 0 and 82. Setting it to the highest power however, while using the on-board antenna, caused communication issues. However it solved the issue that I was hardly able with the shield directly connected on the Arduino to connect to my network. More experimenting should be done to find the right signal strength.

With the setSpeed(19200) subroutine you can change the softSerial() speed of communication between the ESP8266 and Arduino. Most of the time the 9600 default is good enough, but you can change it.

With the softwhoconnected() subroutine it display the IP and MAC of the clients that have logged on to the AP. That does not mean they have started an application that will require a socket ( like tclient)

setSoftTimeout() is used to set a different timeout value for the sockets connected to this server

setsoftIP() will set a new IP address as baseline for the server, if one has been defined

setsoftMAC() will set a new MAC. This MAC can NOT be the same as an device connected to the network (including the hardware Mac of the ESP8266)

The firmware_info() subroutine will obtain the firmware information from the ESP8266.

# 8. Software insights in the driver

A large number of changes have applied for the driver and are documented in a separately.

## 8.1 RAM space
Important for this project was the on-going challenge with RAM space. The final version had a constant warning on low memory available, but all worked well:

Build options changed, rebuilding all
Sketch uses 15350 bytes (47%) of program storage space. Maximum is 32256 bytes.
Global variables use 1360 bytes (66%) of dynamic memory, leaving 688 bytes for local	variables. Maximum is 2048 bytes.

Part of this is because of the extended features and improvements in the driver. There is a way however to reduce that impact in the file PVH_ESP8266WiFi.h, near the top around line 70, you can remove the comments slashes before : //#define ESP_LIGHT 1 to : #define ESP_LIGHT 1.
Save that, recompile the sketch.

This will create a lighter version of the driver by removing features and reduce the buffer (now that these features are removed). Those features are NOT used in this sketch, but might be in other sketches who than fail if you try them later on. It will help for about 120 bytes of RAM.

## 8.2 SoftSerial
A word about SoftSerial as it has caused me a bit of headache when working on the drive

Although with the command AT_GMR you obtain the build information, the Softserial standard receivebuffer is 64.

Defined in …./arduino-nightly/hardware/arduino/avr/libraries/SoftSerial/src/SoftwareSerial.h
  #define _SS_MAX_RX_BUFF 64

That is on the boundary. WHY ? well SoftwareSerial is interrupt driven, as soon as the input level changes, disables that interrupt, trigger a careful time-based checking on the input level to capture the 8 bits, store the byte in it’s buffer and enable interrupt.

This is handled by the SAME processor as the code below, which will get hardly time to read from that softSerial buffer. As such with the call to get firmware the buffer could fill up easily to more than 64 bytes the receivebuffer causing the program to get lost. Extending the buffer to 256 will enable to capture more input, but whether it will overrun is depending on the amount of detected SSID. The buffer could be extended more, but it will take more RAM space.

Note : IN MANY OF MY TEST I HAVE SET THE SOFTSERIAL TO 128 BYTES TO IMPROVE STABILITY.