Overview library calls

This provides an overview of the library calls of PVH_ESP8266.

Paul van Haastrecht
November 2018

All are “int16_t ESP8266CLASS: ” unless indicated differently. (ESP8266Class esp8266)
The calls highlighted in YELLOW are internally used and should not be used by a user
The calls highlighted in BLUE are disabled when #define ESP_LIGHT 1 is set in the PVH_ESP8266Wifi.h. This can be set to reduce the impact on the RAM bytes ( -120 Bytes) and program bytes.
# Defined in PVH_ESP8266_Wifi.cpp
## AutoConnect (int action)
Action: ESP8266_DISABLE
ESP8266_ENABLE

enable or disable autoconnect at power on (default is enable)
this is stored in flash and reserved at the next startup
Return: OK > 0 else error <= 0
## bool enableResetPin(uint8_t pin)
enable hard-reset pin on Arduino for WIFI board to connect ‘reset’ to.
pin can be between 2 and 7, 10 and 13
Return: OK true, ERROR false
## void hard_reset()
perform a hard reset if pin was defined before with enableResetPin
## GetStatusDHCP(bool mode)
get DHCP status
Input
mode : CUR (CURRENT) or DEF (DEFAULT)
Return	0 = BOTH Soft-AP and Station DHCP disabled
 1 = soft-AP enabled
 2 = Station DHCP enabled
 3 = BOTH Soft-AP and Station DHCP enabled
< 0 = error
## SetDHCP(bool mode, int station, int action)
enable or disable DHCP server
Input:
mode : CUR or DEF
station: ESP8266_DHCP_SOFTAP = Soft-AP DHCP
ESP8266_DHCP_STATION = Station DHCP
ESP8266_DHCP_BOTH = soft-AP and Station DHCP
action : SP8266_DISABLE = disable
ESP8266_ENABLE = enable
Return: OK > 0 else error <= 0
## SoftConfigureAP(bool mode, const char * ssid, const char * pwd, int channel, int encoding)
Configure SoftAP
Input :
mode : CUR = CURRENT or DEF = DEFAULT
param ssid:	ssid to set
param pwd:	password to set
param channel:	between channel 0 and 11
param encoding:	type of password encoding

Return: OK > 0 else error <= 0
## SoftGetLocalIP(bool mode, char * ip)
get local IP from SoftAP
Input:
mode : CUR = CURRENT or DEF = DEFAULT
param IP: return the IP from SoftAP

Return : 1 = IP found else error or not found
## SoftGetLocalMAC(bool mode, char * mac)
get local MAC from SoftAP
Input:
mode : CUR = CURRENT or DEF = DEFAULT
param mac: return the MAC from SoftAP

return : OK = 1 + MAC found in mac
error + <= 0 not found
## SoftSetLocalIP(bool mode, char * IP, char *gateway, char *mask)
set local IP on SoftAP
Input
mode :	CUR = CURRENT or DEF = DEFAULT
IP like :	192.168.2.100.
gateway like:	192.168.2.1
mask like:	255.255.255.0
Return:
OK > 0
Error 0<=

This will depend on the last configuration.
If enable static IP, DHCP will be disabled;
If enable DHCP, static IP will be disabled;

Only after ESP8266 station connected to AP, station IP can be got	and inquiried.
## SoftSetLocalMAC(bool mode, char * mac)
Set local mac of SoftAP
Input:
mode :	CUR = CURRENT or DEF = DEFAULT
mac like :	5e:cf:7f:e3:7F:11
Return:
OK > 0
Error 0<=

THE SOFT MAC MUST BE UNIQUE ON THE NETWORK. CAN NOT BE THE SAME
AS THE CURRENT HARDWARE MAC OF THE ESP8266

## int available()
check whether any data available in the serial buffer from the ESP8266

## bool begin(unsigned long baudRate, esp8266_serial_port serialPort)
setup the ESP8266 serial connection.
Input:
Baudrate to use: Default is 9600
serial interface to use : default is SoftSerial, but hardwareSerial1, 2 and 3 are OK

Return : ok = TRUE, error = False
## void clearBuffer()
internal used call to clear the received buffer in the library
## close(uint8_t linkID)
close TCP/UDP connection

Input:
linkID: was used during connect

when ID=5, all connections will be closed (ID=5 has no effect in server mode)

 Return: OK > 0
     ERROR :
 ESP8266_RSP_FAIL : no such connection
 ESP8266_RSP_UNKNOWN : error during communication
 ESP8266_RSP_TIMEOUT : error during communication
## configureTCPServer(uint16_t port, uint8_t create)
configure as a TCP server
Input:
port : port to listen to
create : 1 is create, 0 is delete

Return: OK > 0
 ERROR :
ESP8266_RSP_FAIL : no such connection
ESP8266_RSP_UNKNOWN : error during communication
ESP8266_RSP_TIMEOUT : error during communication
## connect(const char * ssid, const char * pwd)
backward compatibility. Call connect() with CUR = CURRENT.
## connect(const char * ssid)
backward compatibility. Call connect() with CUR = CURRENT.
## connect(bool mode, const char * ssid, const char * pwd)
connect to wireless network
Input:
mode :	CUR = CURRENT or DEF = DEFAULT
ssid :	wireless network name
pwd:	wireless network passwd or empty string
return:
OK: >0
Error: <0 (esp8266_cmd_rsp)
## debug(int act)
set of reset ESP_DEBUG messages from driver
 act :	0 = off
 1 = display commands
 2 = display commands + receive details
## detectAP(char *ssid, char *out, int len, unsigned long timeout)
Will try to detect a single SSID
Input:
ssid :	ssid name to look for (max 20 characters)
out :	buffer to return information (0x0 terminated)
len :	maximum length return buffer
timeout :	timeout in milliseconds
 Return:
OK number of received bytes in out-buffer
ERROR
-1 no characters received (timeout)
-2 character received but did not receive OK. (Buffer can be read for debug)
-4 incorrect length SSID (0 <> 20)
-5 return buffer is to small (Buffer can be read but last byte that fitted is
   overwritten with 0x0 for debug)
-6 incorrect answer received
## EspdigitalRead(uint8_t pin)
Read a digitalpin status on the ESP8266 (implemented by SparkFun)
Input:
pin :	2, 4, 5, 12, 13, 14 or 15

Return: OK : 0 or 1 for LOW or HIGH.
Error : -1.
## EspdigitalWrite(uint8_t pin, uint8_t state)
Set a level on an output pin on the ESP8266 (implemented by SparkFun)
Input:
pin :	2, 4, 5, 12, 13, 14 or15
state :	HIGH or LOW
Return: OK: >0 / Error: <=0
## disconnect()
disconnect from current wifi network

Return:
OK:	0 : disconnect message received,
1 : message not received
Error: <0
## bool echo(bool enable)
echo the commands back or not
 Input
enable : 1 : enable /	0 : disable

Return : ok = TRUE / error = FALSE

This is NOT consistent implemented in the ESP8266 firmware !!
## void flush()
Remove any data pending in the serial connection and the receive buffer
## getAP(char * ssid)
backward compatibility will call getAP() with CUR = CURRENT
## getAP(bool mode, char * ssid)
get connected Access Point name
 Input:
mode :	CUR = CURRENT or DEF = DEFAULT
 Output:
 < 0 = error
 0 = not found
 1 = found and in ssid name of connected AP
## getMode()
backward compatibility will call getMode() with CUR = CURRENT
## getMode(bool stat)
Will obtain current mode (station/ softAP)
Input:
stat : CUR = CURRENT or DEF = DEFAULT
Output:
Success: ESP8266_MODE_STA, ESP8266_MODE_AP, ESP8266_MODE_STAAP
Error: <0 (esp8266_cmd_rsp)
## getVersion(char *ATversion, char *SDKversion, char *compileTime)
obtain the firmware version & build information
input : None
return: OK > 0 and data in Atversion, SDKVersion and compileTime
Error: <=0

## int ESP8266Class::listAP(char *out, int len, unsigned long timeout )
 list all detected AP's (see remarks in PVH_ESP8266_WiFi.cpp)
 Input:
 out:	buffer to store SSID's
 len:	length of buffer
 timeout :	max time to wait for 'OK'
Return: OK : # bytes stored in out.
  Error <= 0
## IPAddress localIP()
Get current local-IP
Input: none
 Output:
 Success: > 0 Device's local IPAddress
 Error: <= 0

 Do not use with SoftAP
## localMAC(char * mac)
backward compatibility calls localMAC with CUR
## localMAC(bool mode, char * mac)
Get local MAC address
mode : CUR = CURRENT or DEF = DEFAULT
Return: OK > 0 : Mac address stored in Mac
  Error <= 0
## int peek()
check whether there is any byte available in serial buffer
## EsppinMode(uint8_t pin, uint8_t mode)
Set pin on ESP8266 as either input or output
  Input:
pin :	2, 4, 5, 12, 13, 14 or 15
mode :
OUTPUT
INPUT
INPUT_PULLUP
Return:
OK: >0 / Error: 0 <=
## ping(IPAddress ip)
perform PING based on IP address structure
## ping(char * server)
perform PING based on character pointer (server or IP address)
## int read()
read bytes from serial interface
## unsigned int readByteToBuffer()
used internally to read a byte from the ESP8266 in the driver buffer
## readForResponse(const char * rsp, unsigned int timeout)
used internally to check the driver buffer for specific response before time-out expires
## readForResponses(const char * pass, const char * fail, unsigned int timeout)
used internally to check the driver buffer for specific responses before time-out expires
## int reset()
Will perform softreset first the ESP8266 and wait for complete. If hard reset pin was enabled a hard reset will be performed is first softreset fails
## int restore()
Will restore the ESP8266 and wait for complete
## void rx_empty(void)
will empty any bytes in the serial buffer from the ESP8266
## char * searchBuffer(const char * test)
will search in the driver received buffer for specific phrase
Input :
test : phrase to look for
Return:
OK : pointer to start of phrase
NOT FOUND : NULL

void sendCommand(const char * cmd, enum esp8266_command_type type, const char * params)
Send a specific command to the ESP8266
## bool setBaud(unsigned long baud)
Backward compatibility. Will call setBaud() with CUR.
## bool setBaud(bool mode, unsigned long baud)
will set the ESP8266 baudrate
Input:
mode:	CUR = CURRENT or DEF = DEFAULT
baud:	baudrate to set between 110 and 115200
Return
OK	: TRUE
ERROR	: FALSE

When softSerial is used, speeds above 56K are nearly impossible
## setMode(esp8266_wifi_mode mode)
Backward compatibility. Will call setMode() with CUR.
## setMode(bool stat, esp8266_wifi_mode mode)
Will set for Station and/or SoftAP Mode
 Input:
 stat : CUR = CURRENT or DEF = DEFAULT
 mode: ESP8266_MODE_STA, ESP8266_MODE_AP, ESP8266_MODE_STAAP
 Return:
 OK >= 0
 Error: <0
## setMux(uint8_t mux)
Internal used to set single or multiple TCP connections
Input:
mux: 1= multiple, 0 = single
Return:
OK >= 0
Error: <0

The different other routines expect multiple connection this is called during begin()
## setTransferMode(uint8_t mode)
input:
mode :
1 enable
0 disable
Return:
OK >= 0
Error: <0

During UART-WiFi passthrough transmission, if it is TCP connection and the TCP	connection breaks, ESP8266 will keep trying to reconnect until “+++” is inputed to quit	from transmission.
If it is a normal TCP transmission and TCP connection breaks, ESP8266 will prompt “	[<link ID>,] CLOSED” , and won’t try to reconnect.
## setlocalIP(bool mode, char * IP, char *gateway, char *mask)
SET local (static) IP address
Input:
mode :	CUR = CURRENT of DEF = DEFAULT)
param IP like :	192.168.6.100
param gateway like :	192.168.6.1
param mask:	255.255.255.0
Return:
OK >= 0
Error: <0

This configuration interacts with AT+CWDHCP related AT commands:
If enable static IP, DHCP will be disabled
If enable DHCP, static IP will be disabled
This will depend on the last configuration
## setlocalMAC(bool mode, char * mac)
SET local MAC address
Input:
mode :	CUR = CURRENT of DEF = DEFAULT)
mac like :	5e:cf:7f:e3:7F:11
Return:
OK	: > 0
Error	: <=0
## sleep(int mode)
set sleep mode for ESP8266
Input:
Mode :

ESP_SLEEP_DISABLE	ESP_SLEEP_LIGHT
ESP_SLEEP_MODEM

Return:
OK	: >0
Error	: <=0

A good article about sleep and the Deep Sleep differences can be found on : https://www.losant.com/blog/making-the-esp8266-low-powered-with-deep-sleep

Also in the extra directory there is a development document with more information

## Deepsleep (uint32_t SleepTime)
 Set the ESP8266 to deepsleep for sleeptime mS.
Input :
SleepTime to maximum 71 min * 60 * 1000 mS
Return:
OK	: >0
Error	: <=0
This will perform a reset and as such all that was connected, options set etc, will be lost.

Requires Hardware wire !!!!!!!!!!!!

The RST pin is held at a HIGH signal while the ESP8266 is running. However, when the RST pin receives a LOW signal, it restarts the microcontroller. Once your device is in Deep-sleep, it will send a LOW signal to GPIO 16 when the sleep timer is up. You need to connect GPIO 16 to RST to wake up ( or reset ) the device when Deep-sleep is over.

ESP8266 GPIO16 is connected to XP0 in the ESP8266 GPIO output connector on the SparkFun ES8266 AT WIFI SHELD. In order for deep sleep to work make a connection between RST and XP0 on the GPIO connector from the ESP8266.
## softAP(const char * ssid, const char * pwd)
Backware compatibility. Will call SoftConfigureAP() with CUR

## status(bool status_new)
will provide feedback about status
Input:
status_new = 1 : new feedback
0: old style feedback (default for compatibility)

This has been changed as the routines feedback is confusing. For the client.cpp a different	feedback was expected, than in the sketch. Looks this was changed during previous	development.

New_feedback
  Return:
OK: 2, 3, 4, or 5 (ESP8266_STATUS_GOTIP, ESP8266_STATUS_CONNECTED,
ESP8266_STATUS_DISCONNECTED, ESP8266_STATUS_NOWIFI)
  Error : <=0

Old_style feedback
return
OK:
connected : 1
not connected : 0
Error <= 0
## tcpBufStatus(uint8_t linkID, char *buf, int size)
read the buffer status and return in buf
input
LinkID : as used during connect
buf	: buffer to return the buffer status string
size	: length of buffer
Return
Ok : # of bytes in buffer
 Error: <=0
 -5 buffer is not large enough
-2 received data, but not OK. Data in buffer for debug
Return Buf example:
1,20,15,10,200,7

1 :<link ID>	: ID of the connection (0~4) for multi-connect
20 :<next segment ID> : next segment ID will be got by AT+CIPSENDBUF
15 :<segment ID of which has sent> : the latest segment that sent (may not succeed);
10 :<segment ID of which sent successfully>: the latest segment that sent successfully;
200:<remain buffer size> : TCP-send-buffer remain buffer size;
 7 :<queue number> : available TCP queue number, it’s not reliable;when queue
      number is 0, no more TCP data can be sent.
## tcpConnect(uint8_t linkID, const char * destination, uint16_t port, uint16_t keepAlive)
make TCP connection
input :
LinkID:	to use for connection
destination :	either IP or server name
Port:	Port on remote server
keepalive	# keepAlive is in units of 500 milliseconds.
return code:
OK :
1 new connection
2 already connected
Error	<= 0 error
## tcpGetTimeout()
Get server timeout value
## tcpResetSeg(uint8_t linkID, uint8_t segID)
Reset segment ID count
input
<link ID>	: ID of the connection (0~4) for multi-connect
SegID	: new Segment ID count
 return :
 OK : 1
 Error : 0
If connection is not established or there are still TCP data wait for sending ERROR.
## tcpSend(uint8_t linkID, const uint8_t *buf, size_t size)
send data over the TCP connections
 input:
linkID is the linkID used at connect
 buf : contains data to sent
 size: number of bytes in buffer (max 2048)
  Return:
OK : # of bytes send
 ERROR : ESP8266_RSP_FAIL (-3)
 Will start sending as soon as number of bytes have been received
## tcpSeqStatus(uint8_t linkID, uint8_t segID)
Check if specific segment sent successfully or not
input
<link ID>	: ID of the connection (0~4) for multi-connect
SegID	: Segment ID to check
 return :
 OK	: 1
 Error	: 0
## tcpSetTimeout(uint16_t timeout)
set timeout ESP8266 as TCP server, will disconnect to TCP client that didn’t communicate
with it even if timeout.
 Input:
timeout : range 0~7200 seconds (0 = never timeout)
Return:
OK >0
Error: <=0
## bool ESP8266Class::tcpStopServer()
stop TCP server that might be running

Return:
OK >0
Error: <=0

 This has to be called at the BEGINNING of a sketch in case a server is to be set with a
different port than potentially	current.
## bool ESP8266Class::test()
will sent an AT to check whether the shield is available
return:
TRUE : response received
FALSE: no response received
## txpower(int mode, int level)
Will set the Transmit power of the ESP8266.
Input:
SET : in steps of 0,25db

Return:
OK >0
Error: <=0

mode = SET : will set the TX power in steps of 0,25db between 0 and 82

Be carefull setting the level too high with the small on-baord antenna as it will not work
all the time and take more power.

## updateStatus()
get TCP status update and store result in internal structure
return:
_status.ipstatus:
2 GOTIP
3 CONNECTED
4 DISCONNECT
5 NO WIFI (returned by softAp all the time (if with valid socket)

It also catches for each channel / LinkID (CIPSTATUS)

 _status.ipstatus[linkId].linkID : the linkID number (a bit overdone..)
 _status.ipstatus[linkId].type : ESP8266_TCP or ESP8266_UDP or unknown
 _status.ipstatus[linkId].remoteIP : the remote IP
 _status.ipstatus[linkId].tetype : I am ESP8266_CLIENT or ESP8266_SERVER;

  This status table is important for client connections
## size_t ESP8266Class::write(uint8_t c)
write a single byte to the serial interface (to ESP8266)

# DEFINED IN PVH_ESP8266_Client.cpp

## int ESP8266Client::available()
check for the number of available bytes from the ESP8266 in the serial buffer.
## int ESP8266Client::connect(IPAddress ip, uint16_t port)
compatibility. Calls connect, add NO-TIME out
## int ESP8266Client::connect(const char *host, uint16_t port)
compatibility. Calls connect, add NO-TIME out
## int ESP8266Client::connect(String host, uint16_t port, uint32_t keepAlive)
compatibility. Makes char* from string
## int ESP8266Client::connect(IPAddress ip, uint16_t port, uint32_t keepAlive)
compatibility. Makes char* from IPAddress
## int ESP8266Client::connect(const char* host, uint16_t port, uint32_t keepAlive)
Here the real TCP connect is happening. Obtain a socket and call TCP_connect
Input
host ( either name or IP)
Port : server port to connect to
Keepalive : in 500ms
Return:
OK >0
Error: <=0
## uint8_t ESP8266Client::connected()
Check that client is still connected, Either to the server (if connected as client) or still on the
server. It will use the socket that is stored in the instance

return:
1 if data available or socket is still connected
 0 not connected anymore
## void ESP8266Client::flush()
flush the input /output buffers
## uint8_t ESP8266Client::getFirstSocket()
Get the next available socket from the table
The whole socket structure is questionable, also because with the Arduino can only
run as single client / server.
Return : OK	: socket
 Error	: -1
## ESP8266Client::operator bool()
This is the response to the statement "if (client)" in the .ino one would expect that it is a
check whether it is larger than zero, but as this is a handle, it is checked whether it still	connected. Return as connected().
## int ESP8266Client::peek()
check whether there is anything in the serial buffer
## int ESP8266Client::read()
read one byte from the ESP8266 / serial buffer
## int ESP8266Client::read(uint8_t *buf, size_t size)
This check first whether there is enough data to fill the buffer and then fill it.
Input:
buf: store read contents
size : expected number of bytes for the buf
Return:
OK	: 1
FAIL	: 0
## uint8_t ESP8266Client::status()
Get the status of the connection
## void ESP8266Client::stop()
Close current socket connection of this instance
## size_t ESP8266Client::write(uint8_t c)
write a single byte to the ESP8266 serial port
## size_t ESP8266Client::write(const uint8_t *buf, size_t size)
write a buffer to the ESP8266 socket with tcpsend()
Input:
buf : byte(s) to write
size: number of bytes to write
Return:
OK : # number of bytes written
Error : 0<=
# DEFINED IN PVH_ESP8266Server.cpp

## ESP8266Client ESP8266Server::available(uint8_t wait)
Checks whether a new client has connected to the server

Input :
wait : number of mS to check on incoming message
Return:
OK	: Client socket handle
FAIL	: 0
## void ESP8266Server::begin()
Create the TCPserver() with the port indicated in creating the handle.
## uint8_t ESP8266Server::status()
get status of the connection
## size_t ESP8266Server::write(uint8_t b)
compatibility . Call write() with size of 1.
## size_t ESP8266Server::write(const uint8_t *buffer, size_t size)
does NOTHING and return 0 as it is never called.
As soon as a client is connected all the communication is over the client() handle