Available new sketch and routines

The following are the example sketches are new in this library:

1. pvh_ESP8266_Shield_client
2. pvh_ESP8266_Shield_softAP_loopback
3. pvh_ESP8266_Shield_softAP_gpio
4. pvh_ESP8266_Shield_server_talkback
5. pvh_ESP8266_Shield_server_loopback
6. pvh_ESP8266_Shield_Server_gpio

Also see
## checkssid(int disp)
available 1, 4, 5
Detect whether requested SSID is available
disp = 1 : will display received information
## connectESP8266()
available 1, 4, 5, 6
Will connect the ESP8266 to a wireless network
uses :
const char mySSID[] = "yourSSIDhere";
const char myPSK[] = "yourPWDhere";
## displayConnectInfo()
available 1, 4, 5
will display the local IP, MAC and connect AP
## errorLoop(int error)
available: ALL
errorLoop prints an error code, reset ESP8266 shield then loops forever.
## firmware_info()
available 1, 2, 4, 5
Get and display firmware version and build information
## handleGPIO(ESP8266Client client)
Available 3, 6

Read the GPIO requests sent by a client and trigger the requested action
## initGPIO()
available 3 ,6

Initialize the GPIO’s for input or output this must be called after the board is initialized
uses:
//////////////////////////////////
// GPIO definitions //
//////////////////////////////////

// CHANGE TO YOUR OWN PINS
#define A_LEDS 4 // max leds on Arduino (must equal the number A_LED entries)
#define ESP_LEDS 2 // max leds on ESP (must equal the number ESP_LED entries)

#define TOTLEDS A_LEDS + ESP_LEDS

uint8_t A_LED[A_LEDS] = {11,12,0,0}; // REPLACE 0 with the pin number for the led on	the Arduino
uint8_t ESP_LED[ESP_LEDS] = {14,12}; // REPLACE 0 with the pin number for the led	on the ESP8266

#define A_BUTS 2 // max Button on Arduino (must equal the number A_BUT	entries)
#define ESP_BUTS 2 // max Button on ESP (must equal the number ESP_BUT	entries)

uint8_t A_BUT[A_BUTS] = {7,0}; // REPLACE 0 with the pin number for the button	on the Arduino
uint8_t ESP_BUT[ESP_BUTS] = {13,0}; // REPLACE 0 with the pin number for the	button on the ESP8266

#define MAX_ADC 5 // maximum ADC ports starting at 0

// structure to capture the led status
struct gpio_led{
 char board; // either A (Arduino) or E (ESP8266)
 uint8_t gpio; // pin number
 int c_state; // current state HIGH or LOW
 int r_state; // request state
 int rate; // number of blinks per minute
 unsigned long next; // when is next blink in milli seconds
} gpio_led;

struct gpio_led LEDS[TOTLEDS];
## initializeESP8266()
Available: ALL
will check that a board is available and initialize.

## Hard_reset()
## enableResetPin()
Available: 5

Part of the initializeESP8266 () routine
## initSoftAP()
available 2, 3
creates a soft Access pooint and will display the default IP, and will call to set new requested softIP and softMac addresses, if requested in the sketch
uses :
////////////////////////////////////////////
// ESP8266Server definition //
////////////////////////////////////////////
char serverSSID[]="testserver"; // or another name
char serverPSK[]="sparkfun"; // or another password
uint16_t server_port = 333;	// or another port
## loopback( ESP8266Client client)
available 2, 5
Will loopback / echo back the data received from a connected client to that cliet loop backtest
## readData(ESP8266Client client, char *out, int len, int retry)
available ALL
Read data from remote and strip +IPD.... header
client = client socket
out =	buffer to store output
len =	length of buffer
retry = retry count for checking

if len is zero, the read data after the header will be displayed
## Server_connect()
available 1,
Will connect a shield as a client to a remote server
uses :
////////////////////////////////////////////////////////////////////////////
// Remote server IP address and port to connect to //
///////////////////////////////////////////////////////////////////////////
char SERVERIP[]= "192.168.1.137";
#define _port 333
## setsoftIP()
available 2
will set a new softAP IP address
uses:
///////////////////////////////////////////////////////////////////////////
// set new newSoftIP[]= "" if no change wanted //
///////////////////////////////////////////////////////////////////////////
char newSoftIP[] = "";
//char newSoftIP[]="192.168.2.100"; // new IP address.
char newSoftGateway[] ="192.168.2.1"; // new Gateway
char newSoftMask[]="255.255.255.0"; // new Mask

## setsoftMAC()
available 2,
will set a new softAP MAC address
uses :
//////////////////////////////////////////////////////
// //
// SOFT MAC SHOULD BE UNIQUE AND NOT EQUAL TO ANY //
// OTHER MAC ON THE NETWORK, INCLUDING THE HARDWARE //
// MAC OF THE ESP8266 //
// //
// set new newSoftMAC[]= "" if no change wanted //
//////////////////////////////////////////////////////
char newSoftMAC[] = "";
//char newSoftMAC[]="5e:cf:7f:e3:7F:11"; // new MAC address.

## setSoftTimeout(uint16_t timeout)
available 2, 3, 6
set server timeout value
## serialTrigger(String message)
available: ALL
serialTrigger prints a message, then waits for something to come in from the serial port.
## serverSetup()
available: 4, 5, 6
Start the shield as a server on the local network and display connection details IP to connect to
## setSpeed(unsigned long speed)
available: 1, 2, 4, 5
set new UART and interface speed once you have done this, the ESP8266 will keep this speed. You have to reset before exiting the program, or unplug the power from the board.
SoftSerial will have most of the time difficulties when setting speed about 56K
## setDHCP()
available: ALL
will set DHCP mode to get it's IP from the AP (opposite to Static)
## setmode(int mode)
available: ALL
Will set the ESP8266 in one of three modes:
ESP8266_MODE_STA	- Station only
 ESP8266_MODE_AP	- Access point only
ESP8266_MODE_STAAP	- Station/AP combo
## setstatic()
available 1, 4, 5
Will set a static IP on the shield
uses :
///////////////////////////////////////////////////////////////////////
// set new static IP if wanted //
// Default : no change wanted //
// Change #define ipaddress "" //
// to something like #define "192.168.1.161"; //
/////////////////////////////////////////////////////////////////////
#define ipaddress "192.168.1.161"

char CLIENTIP[]= ipaddress;
char gateway[]="192.168.1.1";
char mask[]="255.255.255.0";
## soft_server_setup()
available 2, 3
Begin softAP server and display IP to connected
## softwhoconnected()
available 2,
will display who (client IP and MAC) is connected to the softAP (if any)
## talkback( ESP8266Client client)
available 4
Will receive messages from an attached client and sent information that has been input the serial monitor to the attached client. A basic chat.
## SWITCH()
available 3, 6
Will set a digital output high or low depending on the request from the client. The output can be either on the Arduino or the ESP8266.
## BLINK()
available 3, 6
Will set a digital output to switch between high and low depending on the requested frequency from the client.The output can be either on the Arduino or the ESP8266.
## ClrLedAction()
available 3, 6
Clear any previous actions on the GPIO output pins
## DoLedAction()
available 3, 6
Will perform the action set by the BLINK() an SWITCH() routines
## GetAdc()
available 3, 6
Will read an analog pin on the Arduino and sent the status back to the client.
## SetLedPin(int ind)
available 3, 6
Will set led output pin high or low. The output can be either on the Arduino or the ESP8266.
## STATUS()
available 3, 6
Will read a digital input and sent the status (high or low) back to the client. The input can be either on the Arduino or the ESP8266.