Setting up a server with GPIO support

This workbook will describe the steps to setup a server and from a client application set digital pins HIGH or LOW, read analog and digital pins on the Arduino with a SparkFun ESP8266 AT WIFI Shield. It will describe the setup, but also the issues and learning that was obtained during
the project.

Paul van Haastrecht
January 2018

# 1. Software
The test has been performed with the Arduino IDE 1.8.6.

It requires the enhanced version of the Sparkfun ESP8266 AT WIFI shield library from github
https://github.com/paulvha/PVH_ESP8266_AT_Arduino_Library

This needs to be installed as any other IDE library. (there is enough documentation around that) Install the library, restart the IDE.

For the remote client and separate test program is developed in C-language: tclient.c. This program has successfully been used on the Raspberry PI and Ubuntu. It is placed in the “extra” folder of the library.

The GPIO handling is NOT documentation as part of the official ESP8266 AT manual. It is an add-on done by Sparkfun. The documentation is included in the appendix A.
# 2. Hardware

I have used an Arduino Uno and a Sparkfun ESP8266 WIFI Shield. ( https://www.sparkfun.com/products/13287) .

A break-out board for the leds and LDR (for reading analog input)

An extra power-supply. It turned out that my USB was not providing enough power for a stable configuration. So I added a 6V/2A external power supply to the Arduino input.

# 3. Software setup

The server can be setup as a SoftAP (dedicated access point) or as a server in the existing local network. The major difference is that with SoftAP, you are required to login to a separate wireless network / SSID and then connect, where as with a server on the same network, you just have to connect.
## 3.1 Setup server as SoftAP
Obtain the example :
File, Examples, (scroll down) PVH_ESP8266_AT , pvh_ESP8266_Shield_SoftAP_gpio

Save this for your self : File, save-as (give it a name)

Look for :
///////////////////////////////////////////
// ESP8266Server definition //
///////////////////////////////////////////
// (This is only global because it's called in both setup() and loop()).
// CHANGE BELOW TO SET YOUR OWN SSID AND PASSWORD
char serverSSID[]="testserver"; // name
char serverPSK[]="sparkfun"; // password
uint16_t server_port = 330;

You do NOT have to change it, but you can change the SSID name or password. If you change the server_port number, you will also have to change this in tclient.c (PORT_GPIO).

## 3.2 Setup as a server on your network

Obtain the example :
File, Examples, (scroll down) PVH_ESP8266_AT , pvh_ESP8266_Shield_server_gpio

Save this for your self : File, save-as (give it a name)

Look for :
////////////////////////////////////////////
// WiFi Network Definitions //
///////////////////////////////////////////
// Replace these two character strings with the name and
// password of your WiFi network.
const char mySSID[] = "yourSSIDhere";
const char myPSK[] = "yourPWDhere";
uint16_t server_port = 330;

You MUST change to set mySSID to your SSID network name and myPSK to the password in order to connect. If you change the server_port number, you will also have to change this in tclient.c (PORT_GPIO).

## 3.3 Setup GPIO
Look for:

////////////////////////////////
// GPIO definitions //
///////////////////////////////

// CHANGE TO YOUR OWN PINS
#define A_LEDS 4 // max leds on Arduino (must equal the number A_LED entries)
#define ESP_LEDS 2 // max leds on ESP (must equal the number ESP_LED entries)

#define TOTLEDS A_LEDS + ESP_LEDS

uint8_t A_LED[A_LEDS] = {11,12,0,0}; // REPLACE 0 with the pin number for the led on	the Arduino
uint8_t ESP_LED[ESP_LEDS] = {14,12}; // REPLACE 0 with the pin number for the led	on the ESP8266

#define A_BUTS 2 // max Button on Arduino (must equal the number
A_BUT entries)
#define ESP_BUTS 2 // max Button on ESP (must equal the number
ESP_BUT entries)

uint8_t A_BUT[A_BUTS] = {7,0}; // REPLACE 0 with the pin number for the button	on the Arduino
uint8_t ESP_BUT[ESP_BUTS] = {13,0}; // REPLACE 0 with the pin number for the	button on the ESP8266

#define MAX_ADC 5 // maximum ADC ports starting at 0

A_LEDS and ESP_LEDS define the maximum leds in the A_LED[] and ESP_LED[]. The default is 4 leds on the Arduino and 2 on the ESP8266. There is no real need to change that amount, unless you want more. If you change it however A_LED[] and/or ESP_LED[] need to be changed to the same amount of entries.

In the A_LED[] and ESP_LED[] you define the pin number to which the LED is connected on either the Arduino (A_LED[]) or the ESP8266 (ESP_LED[]). In the default configuration we are using 2 leds on pins on the Arduino (11 and 12). The other 2 are not used and set to 0 to indicate there are not used. Change this to your setup and entries not used should be set to 0. On the ESP8266 we are using 2 leds (14 and 12). If you would only connect to pin 14, set the second entry to 0.

Do not change TOTLEDS, that is an automatic calculation.

A_BUTS and ESP_BUTS define the maximum input pin in A_BUT[] and ESP_BUT[]. The default is 2 input on the Arduino and 2 on the ESP8266. There is no real need to change that amount, unless you want more.

In the A_BUT[] and ESP_BUT[] you define the pin number to which the button is connected on either the Arduino (A_BUT[]) or the ESP8266 (ESP_BUT[]). In the default we are using 1 button on pins on the Arduino (7). The other is not used and set to 0. Change this to your setup. Entries not used should be set to 0. On the ESP8266 we are using 1 button (13) and the second entry is set to 0.

The MAX_ADC will set the maximum number of input ports. It does not take a pin number but will use the ADC0 – ADC5 on the Arduino. While the ESP8266 has an ADC pin, the firmware implementation by Sparkfun on the ESP8266 does not support reading that value.

Where A_LED[] and ESP_LED[] pins are set for OUTPUT, the A_BUT[] and ESP_BUT[] pins are set for INPUT_PULLUP.

WARNING : THERE IS NO CHECK WHETHER THE SAME PIN IS USED FOR BOTH INPUT, OUTPUT OR ADC. THE PROGRAM WILL SET THE INPUTS LAST AND AS SUCH THEY WILL BECOME INPUT.

## 3.4 Setup Debug
A new feature with this driver is to see what information is exchanged between the Arduino and ESP8266. In the setup(),

  // enable debug data from driver
  // (0 = disable (default), 1 = show commands, 2 = detailed)
 esp8266.debug(0);

0 is default (actually you do not need to call it),
1 will show which commands are sent to the ESP8266. This will align with the ESP8266 AT
    documentation (which is also stored in the “extra” directory of the library)
2 will show next to the commands, the feedback from the ESP8266. The format for each line:
btb C H B \n
btb: byte to buffer routine
C : character as received
H : hex value of the character
B : buffer index

With option 2 it might be hard to see at the serial output as a lot of information is flowing over the screen, but you can pause that and scroll back by disabling auto scroll bottom left in the IDE serial monitor.

## 3.5 Setup Client software
The tclient.c has been tested under Linux on the Raspberry Pi-3 and Ubuntu. To compile on the Raspberry Pi: cc -o tclient tclient.c. With little changes (e.g. getopt) it could be made to work
also under windows.
# 4. Hardware setup
## 4.1 Setup ESP8266

Set the switch for the serial connection on the ESP8266 to SW (softserial), otherwise it will not work. I have connected the Arduino Stackable Header Kit, so it connects directly to the board. I had issues with that (see hardware learnings)

In my situation the configuration was unstable as the USB was not able to provide enough power from my Ubuntu PC. Hence I connected an external power supply ( 6V / 2A). It became much better, but still my ESP8266 was not always reacting as I hoped. (see hardware learnings)

## 4.2 setup GPIO
Make sure to connect the Leds to the output pins that you have defined in A_LED[] or ESP_LED[]. I normally put a 470 ohm resistor in serial to ground to keep the current flowing low.

Connect a button or cable to the input pins defined in A_BUT[] and ESP_BUT[]. As these are set with an internal pull-up resistor, you only have to connect those to GND to see the impact when reading.

If the ADC is used, you could use an LDR to 3V3 with a serial resistor of 4k7ohm to ground. Connect their connection point to the ADC0 (or other ADC input).

# 5. Starting Software
## 5.1 Starting as SoftAp

After setting the parameters, compile and loading to the Arduino. Then open the serial monitor for 9600 baud connection (default)

The first message is : Press any key to begin.

This is waiting on your presence . After pressing <enter> the following sequence will appear

initializing ESP8266
ESP8266 Shield Present
Stop any server running + board reset ( 2 - 3 seconds)
initializing Access Point
Mode set to SoftAP and station
initializing GPIO

Press any key to start server.

After pressing <enter> you will see something like:

Server timeout 300
Connect to address : 192.168.4.1 port for GPIO test : 330

Watch the IP address , as you need that later on for the command line on your client application

## 5.2 Starting as server on your network
After setting the parameters, compile and loading to the Arduino. Then open the serial monitor for 9600 baud connection (default)

The first message is : Press any key to begin.

This is waiting on your presence . After pressing <enter> the following sequence will appear

initializing ESP8266
ESP8266 Shield Present
Stop any server running + board reset ( 2 - 3 seconds)
start connecting
Mode set to station
Connecting to <YOUR_SSID>
initializing GPIO

Press any key to start server.

The line : Connecting to <YOUR_SSID>, will show the SSID you have set for your network. If that connection fails all the time, check your network SSID and password. If that keeps failing, maybe you have a weak signal. You could try to use the pvh_ESP8266_Shield_talkback.ino, as that will display whether there requested SSID could be detected. I had to remove that from this sketch as I was already running low on RAM bytes.

After pressing <enter> you will something like:
Server timeout 300
Server started! Go to 192.168.1.107 port : 330

Watch the IP address , as you need that later on for the command line on your client application

NOTE
Sometimes however, much more than I wanted, my board was not reacting (this can be seen with setting debug to 2). If it ends with something like:
Error during stopping server.
Error: 0
Looping forever.
The best way is to close the serial monitor, and re-open the serial monitor and try again. Sometimes I had to do so 3 times, sometimes I had to re-compile and reload, sometimes I had to remove the USB (and power connection) for a hard reset. Using the reset switch does not do ANYTHING, other than reboot the Arduino.

WARNING: IF YOU REMOVE AND REAPPLY POWER, MAKE SURE THAT THE SERIAL MONITOR IS CLOSED. OTHERWISE IT WILL NOT RE-CONNECT ON THE SAME USB PORT

## 5.3 Starting with client
ONLY if you have setup for SoftAP, you must login your wireless to this access point from your the remote PC/Raspberry Pi .
WARNING : You will have to check this every time you restart the program !!
Your remote PC/Raspberry Pi must be connected wireless (as this is a wireless access point) and look for the SSID with the name you selected (default: testserver). Select that and enter the password that you have set (default: sparkfun). It will take sometime to connect.

If it can not find the SSID, try refresh the list, try to get closer to the Arduino and shield, change the angle a bit. If that does not work, look whether you see the SSID on your smart phone. There are also special programs that show available SSID’s. If NOT found, restart the server, close the serial monitor and start again. If you detect the SSID, but can not login, check your password, check the signal strength etc.

To start the client connection, type ./tclient -g <IP-address>
Taken the examples above
running as SoftAp : ./tclient -g 192.168.4.1
running as Server : ./tclient -g 192.168.1.107
The port (330) is hard coded in the program and chosen as you select -g option.
# 6. Using software
Once you started the client on the serial monitor from the Arduino you should see
Client detected
GPIO handling client connected!

If NOT, while the client shows the menu, select 9 <enter> on the client and try to connect the client again.

NOTE:
If the client show “connect error”, most of the time the ESP8266 server has not been started and waiting on you to press enter. (happened to me more than once).

WARNING: IT WILL TAKE SOMETIME BEFORE THE SERVER STARTS, BUT ALSO SOMETIME AFTER THE CLIENT DISCONNECT AND CAN CONNECT AGAIN.
WAIT 10 SECONDS AFTER SERVER START OR DISCONNECT TO (RE) CONNECT.

On the client you should see the following menu :

What action do you want to do ?
1 swith a led on or off
2 set a led for blinking
3 read a button
4 read an ADC value
9 exit

If your action is 1, 2 or 3 the next question is :

On which board is it connected
1 Arduino
2 ESP8266
9 exit

If the action is 1 or 2: it will ask for : Which LED ?
In case action 1, it will then ask: ON or OFF
In case action 2, it will then ask: How many seconds ON/OFF

In case of action 3 or 4 it will ask : Which input pin?

The next step it will show a command like (switch on led 1 on the Arduino)
Sending : SWITCH(A_LED1,ON)

On the server you should now see :
Received : SWITCH(A_LED1,ON)
Sending feedback : OK

The answer that should follow is received Feedback : OK

If you get “Nothing received” the server has not answered in time. Check that is does show on the server that you are (still) connected.

# 7. Software insights in the Sketch
Sharing some aspects of the software to share.

In this sketch a number of new features that are available in pvh_ESP8266_Shield_backlogging or pvh_ESP8266_Shield_talkback.ino have been removed. I was running low on RAM memory.
See Software insights in the driver as well

Setup()
The esp8266.debug() See the debug information in the chapter setting up software

initializeESP8266()
The esp8266.tcpStopServer() is a new feature. When setting up as a server we want to be able to potentially switch to different port than the current. This can only be done if we first STOP a potential current server. Stopping means also a reset, which takes time and it is important to wait for proper reset.

The esp8266.txpower(ESP8266_POWER_SET, 40) is a new feature. It allows to set the transmitter power in steps of 0.25db. The value can be between 0 and 82. Setting it to the highest power however, while using the on-board antenna, caused communication issues. However it solved the issue that I was hardly able with the shield directly connected on the Arduino to connect to my network. More experimenting should be done to find the right signal strength.

GPIO LED handling
To get a stable blink, while still looping for new commands coming from the network client, a different approach had to be implemented than the standard blink ON,delay,OFF, delay… sequence. Next to that I wanted to be able to blink leds at a different speed and stop blinking when setting a led ON or OFF.

I have defined a new structure to keep track of status and changes, with an entry for each LED PIN:

// structure to capture the led status
struct gpio_led {
 char board; // either A (Arduino) or E (ESP8266)
 uint8_t gpio; // pin number
 int c_state; // current state HIGH or LOW
 int r_state; // request state
 int rate; // number of blinks per minute
 unsigned long next; // when is next blink in milli seconds
} gpio_led;

struct gpio_led LEDS[TOTLEDS];

initGPIO() will set the pins on either the Arduino or the ESP8266 for output, based on the A_LED[] & ESP_LED[], or input_pullup, based on A_BUT[] & ESP_BUT[]. It will also set the LEDS-entries as available.

ClrLedAction() will initialize this table starting each new client connection. If any of the entries was in use it will set the output low by calling SetLedPin(index) and mark the entry as free.

SetLedPin(index) the index is the offset in LEDS. It will set a pin to the requested output level based on r_state on either the Arduino or the ESP8266. It will then setting the current state (c_state) to indicate that level.

handleGPIO(client) is called as soon as a new client has connected to the server. Given the structure it can only one client at the time. It will try to read input from the client and based on that call the action-subroutine to switch(), blink(), status() or getADC(). At the end of each loop, it will call DoLedAction() to perform any action that was set by the action-subroutine switch() or blink(). It will continue to be looping as long as the connection to the client is in place. There is a disconnect of 300 seconds, 5 minutes, set during server_setup()

FindLedEntry(char board, int pin) will search the LED-array to find an existing entry for the board (either Arduino or ESP8266) and led-pin or return the next available one.

FindBoardLed() this will be called from switch() or blink() to determine on which board the led is located (either Arduino or ESP8266), whether the led-pin is valid (within limits and set in either A_LED[] or ESP_LED[], obtain an entry in the LED-array by calling FindLedEntry() and set the led-pin/gpio and board in that entry.

Switch() will call FindBoardLed(). It will then indicate that is non-blinking and the led-pin should be set HIGH or LOW depending on the client’s request. It will NOT set the pin itself, but indicate in the LED-array. The real action is performed with DoLedAction().

blink() will call FindBoardLed(). It will then indicate that the led-pin should blink with the rate as requested by the client and the next moment of switching output level (now). It will NOT set the pin itself, but indicate this the LED-array. The real action is performed with DoLedAction().

DoLedAction() is called at the end of each loop to check for client input. It will read all the LED-array entries and if an entry has a led-pin, perform the requested action.
If the rate is non-zero the action is to blink. It will check whether the timeout as expired and if so set the r_state to the opposite output level for of the current state. It will then calculate and set the next timeout.
The next step is to check with r_state is different than c-state (e.g. set for blinking or by switch()) and call SetLedPin(index) to set the new level on the output.
# 8. Software insights in the driver
A large number of changes have applied for the driver and are documented in a separately.

## 8.1 RAM space
Important for this project was the on-going challenge with RAM space. The final version had a constant warning on low memory available, but all worked well:

Sketch uses 16468 bytes (51%) of program storage space. Maximum is 32256 bytes.
Global variables use 1522 bytes (74%) of dynamic memory, leaving 526 bytes for local	variables. Maximum is 2048 bytes.

Part of this is because of the extended features and improvements in the driver. There is a way however to reduce that impact in the file PVH_ESP8266WiFi.h, near the top around line 70, you can remove the comments slashes before : //#define ESP_LIGHT 1 to : #define ESP_LIGHT 1.
Save that, recompile the sketch.

This will create a lighter version of the driver by removing features and reduce the buffer (now that these features are removed). Those features are NOT used in this sketch, but might be in other sketches who than fail if you try them later on. It will help for about 120 bytes of RAM.

## 8.2 SoftSerial
A word about SoftSerial as it has caused me a bit of headache when working on listap()

Although with the command AT+CWLAP you can obtain the information from ALL the SSID the ESP866x discovered, within Softserial the standard receivebuffer is 64.

Defined in …./arduino-nightly/hardware/arduino/avr/libraries/SoftSerial/src/SoftwareSerial.h
  #define _SS_MAX_RX_BUFF 64

That is TOO small and it will overrun. WHY ? well SoftwareSerial is interrupt driven, as soon as the input level changes, disables that interrupt, trigger a careful time-based checking on the input level to capture the 8 bits, store the byte in it’s buffer and enable interrupt.

This is handled by the SAME processor as the code below, which will get hardly time to read from that softSerial buffer. As such with the call to get ALL SSID, or anything more than 64 bytes the receivebuffer will be full in no time, causing the program to get lost. Extending the buffer to 256 will enable to capture more input, but whether it will overrun is depending on the amount of detected SSID. The buffer could be extended more, but it will take more RAM space.

It is better to use detectAP() to check whether a certain SSID is discovered OR extend the
softserial buffer size

Note : IN MANY OF MY TEST I HAVE SET THE SOFTSERIAL TO 128 BYTES TO IMPROVE STABILITY.

# Appendix A. Sparkfun ESP8266 GPIO implementation

Function	Command	Example	Notes
Pin Mode	AT+PINMODE=<pin>,<mode>	AT+PINMODE=5,o	Mode: / o: OUTPUT / i: INPUT / p: INPUT_PULLUP
Digital Write	AT+PINWRITE=<pin>,<state>	AT+PINWRITE=5,h	State: / h: HIGH / l: LOW
Digital Read	AT+PINREAD=<pin>	AT+PINREAD=0	Response: 0 or 1 for LOW or HIGH.

Source : https://learn.sparkfun.com/tutorials/esp8266-wifi-shield-hookup-guide